## Slide 1: MIDTERM presentation Barcode CHECKER 7681
By: Omar Sharafy, Muhammad Biadsy
Instructor: Mony Orbach
Lab: HSDSL
Spring Semester 2024

## Slide 2: BACKGOUND & Motivation
In Hospitals, samples are collected from patients.
each sample is labeled with barcode stickers, unique to each patient.
The samples are manually checked in the lab against patient details in the computer system.
the numerous number of samples received daily can lead to confusion and mix-ups between samples, potentially resulting in life-threatening medical errors.

## Slide 3: Goals
Development of an easy to carry and simple tool that solves the problem of confusion in the hospital laboratory .
The tool should
Compare between barcodes and give us a clear result.
communicatee via Wi-Fi with a computer.
Save barcodes.
Mobile, compact and Re-chargeable.

## Slide 4: Components & work development
Components :
Barcode reader (Including built in buzzer).
Esp32.
Screen - SPI TFT LCD.
Realtime clk.
Charger – USB Type-C.
Sd card.
LEDs.
Work development :
Arduino developing environment.
Notes: Barcode Dimension 2.6*5.6*5.6cm
Screen 4.2 * 3.9 inches

## Slide 5: Block diagram
Target Barcode
Outsider PC
User
OUR DEVICE
WI-FI
Interface

## Slide 6: Mod of work Diagram
start
Scan the “Golden barcode” & save it to the SD card
Scan a barcode we want to compare to the Golden
Get the result via sound + screen, and save the result
Scan the target barcode and save it to the SD Card

## Slide 7: Block diagram
LEDs
Screen
ESP32
SD card
Power Supply Unit
RTC
Barcode reader
Buzzer
Target Barcode
Outsider PC
User
WI-FI Interface
Charger
PMU
Arduino

## Slide 8: Power MNAGMENT UNIT
DC/DC Converter
DC/DC Converter
Input 5V
Output 5V
Output 3.3V
For Barcode reader
For ESP32 & other components

## Slide 9: ESP32
Includes many drivers that make programming easier.
Advantages over Arduino nano: speed and memory
2 cores.
 | ESP32 | Arduino nano
Clock rate | 80 MHz | 16 MHz
Memory size | 520 KB SRAM 4 MB flash memory | 2 KB SRAM 32 KB flash

## Slide 10: Arduino developing environment
Supports the ESP32.
Rich collection of libraries for various sensors and communication protocols.
Easy to use and quickly start coding.
Supports wide range of applications.

## Slide 11: Barcode reader
2D Barcode scanner.
Built in buzzer that we can adapt it to our project.
Supports Arduino development Environment.
Notes: 125 mA = I
Built in buzzer
Built in led

## Slide 12: Gant diagram
layout
Code bring - up
Designing a case via 3D Printer
Debug
| 13august24 | 20august24 | 27august24 | 3sep24 | 10sep24 | 17sep24 | 24sep24 |
Today
Final presentation