## Slide 1: MIDTERM presentation Barcode CHECKER 7681
By: Omar Sharafy, Muhammad Biadsy
Instructor: Mony Orbach
Lab: HSDSL
Spring Semester 2024

## Slide 2: BACKGOUND & Motivation
In Hospitals, Samples are collected from patients and labeled with unique barcode stickers.
Visual Checking: In the lab, samples are checked visually against patient barcodes in the system.
Potential Issues: High number of samples can cause confusion and mix-ups, resulting in issuing wrong meds and treatments.
Difficulty in Comparison: Visual comparison of barcodes is challenging for lab personnel (Or any human for that matter).

## Slide 3: Goals
Development of an easy to carry and simple tool that solves the problem of confusion in the hospital laboratory .
The tool should
Compare between barcodes and give us a clear result.
communicatee via Wi-Fi with a computer.
Save barcodes.
Mobile, compact and Re-chargeable.

## Slide 4: Components & work development
Components :
Barcode reader (Including built in buzzer).
Esp32.
Screen - SPI TFT LCD.
Realtime clk.
Charger – USB Type-C.
Sd card.
LEDs.
Work development :
Arduino developing environment.
Notes: Barcode Dimension 2.6*5.6*5.6cm
Screen 4.2 * 3.9 inches

## Slide 5: TOP VIEW Block diagram
Target Barcode
Outsider PC
User
OUR DEVICE
WI-FI
Interface

## Slide 6: Mod of work Diagram
start
Scan the “Golden barcode” & save it to the SD card
Scan a barcode we want to compare to the Golden
Get the result via sound + screen, and save the result
Scan the target barcode and save it to the SD Card

## Slide 7: Block diagram
LEDs
Screen
ESP32
SD card
Power Supply Unit
RTC
Barcode reader
Buzzer
Target Barcode
Outsider PC
User
WI-FI Interface
Charger
PMU
Arduino
Switches

## Slide 8: Power MNAGMENT UNIT
DC/DC Converter
DC/DC Converter
Input 5V
Output 5V
Output 3.3V
For Barcode reader
For ESP32 & other components

## Slide 9: Communication Diagram
Display
PCB
SD card
Barcode Sensor
ESP32
SPI
UART
SPI
Switches
Analog
Buzzer
Analog
LEDs
Analog

## Slide 10: ESP32
Includes many drivers that make programming easier.
Advantages over Arduino nano: speed and memory
2 cores.
 | ESP32 | Arduino nano
Clock rate | 80 MHz | 16 MHz
Memory size | 520 KB SRAM 4 MB flash memory | 2 KB SRAM 32 KB flash

## Slide 11: Arduino developing environment
Supports the ESP32.
Rich collection of libraries for various sensors and communication protocols.
Easy to use and quickly start coding.
Supports wide range of applications.

## Slide 12: Barcode reader
2D Barcode scanner.
Built in buzzer that we can adapt it to our project.
Supports Arduino development Environment.
Notes: 125 mA = I
Built in buzzer
Built in led

## Slide 13: Gant diagram
layout
Code bring - up
Designing a case via 3D Printer
Debug
| 13august24 | 20august24 | 27august24 | 3sep24 | 10sep24 | 17sep24 | 24sep24 |
Today
Final presentation