## Slide 1: MIDTERM presentation Barcode CHECKER 7681
By: Omar Sharafy, Muhammad Biadsy
Instructor: Mony Orbach
Lab: HSDSL
Spring Semester 2024

## Slide 2: BACKGOUND & Motivation
In Hospitals, Samples are collected from patients and labeled with unique barcode stickers.
Visual Checking: In the lab, samples are checked visually against patient barcodes in the system.
Potential Issues: High number of samples can cause confusion and mix-ups, resulting in issuing wrong meds and treatments.
Difficulty in Comparison: Visual comparison of barcodes is challenging for lab personnel (Or any human for that matter).

## Slide 3: Goals
Development of an easy to carry and simple tool that solves the problem of confusion in the hospital laboratory .
The tool should :
Compare between barcodes and give us a clear result.
Save the scanned barcodes and the results.
Mobile, compact and Re-chargeable.
communicatee via Wi-Fi with a computer.
Provide a log with all the scanning results.

## Slide 4: Components & work development
Components :
Barcode reader (Including built in buzzer).
Esp32.
Screen - SPI TFT LCD.
Realtime clk.
Charger – USB Type-C.
Sd card.
LEDs.
Work development :
Arduino developing environment.
Notes: Barcode Dimension 2.6*5.6*5.6cm
Screen 4.2 * 3.9 inches

## Slide 5: TOP VIEW Block diagram
Target Barcode
Outsider PC
User
DEVICE
WI-FI
Interface

## Slide 6: Mod of work Diagram
start
Scan the “Golden barcode”
Scan the target barcode
Show the result via sound + screen & LED’s, and save the result
After each comparison, we will log both the Golden and target barcodes, along with the results and the date of scanning. This will create a comprehensive record that allows us to trace any potential errors efficiently.
When the device’s memory is full, the user can decide if he wants to override some results or delete all and start a new log.

## Slide 7: Block diagram
ESP32
SD card
Power Supply Unit
RTC
Outsider PC
WI-FI Interface
Charger
PMU
Switches
Screen
Buzzer
LEDs
Barcode reader

## Slide 8: Power MNAGMENT UNIT
DC/DC Converter
DC/DC Converter
Input 5V
Output 5V
Output 3.3V
For Barcode reader & screen
For ESP32 & other components

## Slide 9: Communication Diagram
Display
ESP32
SD card
Barcode Sensor
SPI
UART
SPI
RTC
I2C
Outsider PC
WI-FI

## Slide 10: ESP32
Includes many drivers that make programming easier.
Advantages over Arduino nano: speed and memory
2 cores.
 | ESP32 | Arduino nano
Clock rate | 80 MHz | 16 MHz
Memory size | 520 KB SRAM 4 MB flash memory | 2 KB SRAM 32 KB flash

## Slide 11: Barcode reader
2D Barcode scanner.
Built in buzzer that we can adapt it to our project.
Supports Arduino development Environment.
Notes: 125 mA = I
Built in buzzer
Built in led

## Slide 12: Arduino developing environment
Supports the ESP32.
Rich collection of libraries for various sensors and communication protocols.
Easy to use and quickly start coding.
Supports wide range of applications.

## Slide 13: Until now
Define objectives.
E.E Scheme.
Layout.

## Slide 14: Layout - TOP

## Slide 15: Layout - BOTTOM

## Slide 16: Gant diagram
layout
Software development
Designing a case via 3D Printer
Debug
| 18Aug24 | 25Aug24 | 1Sep24 | 22Sep24 | 29Sep24 | 5Oct24 | 19Oct24 |10Nov24
Today
Final presentation
Exams
Hardware bring-up
Integration