## Slide 1: FINAL presentation Barcode CHECKER 7681
Students: Omar Sharafy, Muhammad Biadsy
Instructor: Mony Orbach
Lab: HSDSL
Spring Semester 2024

## Slide 2: BACKGOUND & Motivation
In Hospitals, Samples are collected from patients and labeled with unique barcode stickers.
Visual Checking: In the lab, samples are checked visually against patient barcodes in the system.
Potential Issues: High number of samples can cause confusion and mix-ups, resulting in issuing wrong meds and treatments.
Difficulty in Comparison: Visual comparison of barcodes is challenging for lab personnel (Or any human for that matter).

## Slide 3: Goals
Development of an easy to carry and simple tool that solves the problem of confusion in the hospital laboratory .
The tool should :
Compare between barcodes and give us a clear result.
Provide a log with all the scanning results.
Mobile, compact and Re-chargeable.
communicatee via Wi-Fi with a computer to view results.

## Slide 4: Components & work development
Components :
Barcode reader (Including built in buzzer).
Esp32.
Screen - SPI TFT LCD.
Realtime clk.
Charger – USB Type-C.
Sd card.
LEDs.
Work development :
Arduino developing environment.
Notes: Barcode Dimension 2.6*5.6*5.6cm
Screen 4.2 * 3.9 inches

## Slide 5: TOP VIEW Block diagram
Target Barcode
Outsider PC
User
DEVICE
WI-FI
Interface

## Slide 6: Mod of work Diagram
start
Scan the “Golden barcode”
Scan the “Target barcode”
Show the result via screen & LED, and save the result
After each comparison, we will log both the Golden and target barcodes, along with the results, time and date of scanning.
The user can change the Golden barcode at any time.
The user can scan continuously Target barcodes.
The log record to the last result can be accessed via WI-FI.

## Slide 7: Block diagram
ESP32
SD card
Power Supply Unit
RTC
Outsider PC
WI-FI Interface
Charger
PMU
Switches
Screen
Buzzer
LED
Barcode reader

## Slide 8: Power MNAGMENT UNIT
DC/DC Converter
DC/DC Converter
Input 5V
Output 5V
Output 3.3V
For Barcode reader
For ESP32 & other components

## Slide 9: Communication Diagram
Display
ESP32
SD card
Barcode Sensor
SPI
UART
SPI
RTC
I2C
Outsider PC
WI-FI

## Slide 10: ESP32
Includes many drivers that make programming easier.
Advantages over Arduino nano: speed and memory
2 cores.
 | ESP32 | Arduino nano
Clock rate | 80 MHz | 16 MHz
Memory size | 520 KB SRAM 4 MB flash memory | 2 KB SRAM 32 KB flash

## Slide 11: Barcode reader - GM810
2D Barcode scanner.
Ledes to scan the barcodes easily.
Built in buzzer while scanning.
Supports UART that can be controlled via Arduino development Environment & communicate with ESP32.
powered with 5V.
Notes: 125 mA = I
Built in buzzer
Built in led

## Slide 12: Arduino developing environment
Supports the ESP32.
Rich collection of libraries for various sensors and communication protocols.
Easy to use and quickly start coding.
Supports wide range of applications.

## Slide 13: Display - 3.2 TFT SPI 240x320 V1.0
3.2 inch.
240X320 pixels.
Supports SPI that can be controlled via Arduino development Environment & communicate with ESP32.
Can be powered with 3.3V.

## Slide 14: Electrical schematic

## Slide 15: Layout - TOP

## Slide 16: Layout - BOTTOM

## Slide 17: Testing
Each component tested separately without the PCB successfully.
While testing the components on the PCB, Some of mistakes was founded at the display & SD connection.
So, we forced to use wires to correct the connections.

## Slide 18: Example - Screen test

## Slide 19: Final design
Cheap device about 50$ as we aimed.
Small device as we aimed:
  The display, switches & leds placed at the PCB.
  Barcode will be placed close to the PCB at the opposite side of the display.
  The SD placed at the PCB hidden in the box.
  Battery will be hidden in the box close to the PCB top side.
Device that meets all the functional requirements.

## Slide 20: real device

## Slide 21
Strat screen
Scan golden Barcode screen
Scan target Barcode Screen
Different Barcodes screen

## Slide 22
Blue LED, indicates identical barcodes
Identical Barcodes screen
Different Barcodes WI-FI page
Identical Barcodes WI-FI page

## Slide 23: Introducing the device

## Slide 24: conclusions
Compare 2D barcodes Golden with Target barcode, identical/different.
One led instead of two.
One switch instead of three.
Display with results.
WIFI interface as an AP and web page.
Chargeable with type-C cable.
SD that holds the log of the comparisons results.

## Slide 25: Proposal for a follow-up project
Create An accessible server easily to search barcodes and find mistakes.
Connect the device to the server to save the results.
New PCB with the corrected electrical schematic.
Application to control the device:
  Access SD results data
  Change mode of scanning
  Set the device
  Alternative screen results

## Slide 26: Thank you for listening we appreciate your help and guidance!